Figure 1. Connections to the AD Converter. The numbers with gray background indicate the number of the pin on the parallel port

Figure 2. Schematics of the thermometer-indicator system. All connections to the ADC0804 are not shown for clarity.

## Control of the ADC0804

Make sure that the parallel port is in the bi-directional mode and stays like this during the measurements.

Voltages at pin 2 and pin 3 (on the ADC) must be +5V before the conversion.

- To start a new conversion, we must make WR (pin 3 on the ADC) 0 V and then return it to +5 V state. The conversion starts when pin 3 goes high (rising edge triggered)

- Wait until INTR (pin 5 on the ADC) goes to 0 V. (When the conversion process is done, this pin goes to 0.)

- When pin 5 goes low, we must make RD (pin 2 on the ADC) go to 0 V to load the new value to the digital outputs (pin 11 to 18 on the ADC)

- Read the values on the digital outputs into the parallel port

- Lastly, return RD (pin 2 on the ADC) to the +5 V state

The next conversion can be done with repeating the steps 1 to 5.

# Text boxes

1

10

9

8

7

6

5

4

3

2

11

12

13

14

15

16

17

18

19

20

+ 5V

GND

GND

GND

GND

GND

10 k(

150 pF

1

16

15

analog voltage input

Digital Input

pins 2 through 9

on the parallel port

# ADC0804

1 k(

14

ADC0804

GND

2 k(

GND

LM335

6

+ 5V

LED